## Slide 1: Simple calculator
Due: 4/19 Friday 13:30-15:00

## Slide 2: Small computer
Let’s consider a CPU, which has eight 32-bit registers r0-r7 and a 256-byte memory.
In this project, you need to implement a calculator. The input is a list of expressions consisting of integers, operators(+, -, *, /, =, &, |, ^), and at least three variables x, y, z(x, y, z exist in the begin, and some local variables will appear in the input file); and the output is a list of assembly codes.
The instructions of the CPU are listed in the next pages. The time to execute each instruction (in clock cycles) is also listed.

## Slide 3: Instruction Set Architecture (I)
Opcode | Operand1 | Operand2 | Meaning | Cycles
MOV | Register1 | Register2 | Move data from register2 to register1 | 10
 | Register1 | Constant | Set the value of register1 constant | 10
 | Register1 | [Addr2] | Move the data (4 bytes) in memory addressed Addr2 to register1. Note that Addr2 must be a multiple of 4. | 200
 | [Addr1] | Register2 | Move the data (4 bytes) from register2 to the memory addressed Addr1. Note that Addr1 must be a multiple of 4. | 200

## Slide 4: Instruction Set Architecture (II)
Opcode | Operand1 | Operand2 | Meaning | Cycles
ADD | Register1 | Register2 | Add the values in register1 to register2 and store the result in register1 | 10
SUB | Register1 | Register2 | Subtract the value in register2 from the value in register1, and store the result in register1. | 10
MUL | Register1 | Register2 | Multiply the values in register1 to register2 and store the result in register1 | 30
DIV | Register1 | Register2 | Divide the value in register1 by the value in register2, and store the result in register1. Note it is the integer division. | 50
EXIT | Constant |  | Stop the program with a constant signal, whose value is specified as follows. 0: exit normally 1: the expression cannot be evaluated | 20

## Slide 5: Instruction Set Architecture (III)
Opcode | Operand1 | Operand2 | Meaning | Cycles
AND | Register1 | Register2 | Binary and the values in register1 to register2 and store the result in register1 | 10
OR | Register1 | Register2 | Binary or the values in register1 to register2 and store the result in register1 | 10
XOR | Register1 | Register2 | Binary exclusive or the values in register1 to register2 and store the result in register1 | 10
The priority of AND, OR, XOR are the same as ADD, SUB in this project.

## Slide 6: A complete grammar rules
The valid way to arrange the token
statement := END | expr END
expr := term expr_tail
expr_tail := ADD_SUB_AND_OR_XOR term expr_tail | NiL
term := factor term_tail
term_tail := MUL_DIV factor term_tail|NiL
factor := INT | ADD_SUB INT | ADD_SUB ID | ID ASSIGN expr| ID | LPAREN expr RPAREN

## Slide 7: Variables
The initial value of variables, x, y, and z, are stored in memory [0], [4], and [8] respectively. You need to read those initial values first.
If a variable first appears in the left hand side of an assignment operation, it is valid and can be used in the right hand side in the future; if a variable first appears in the right hand side, it is invalid and the output should print EXIT 1

## Slide 8: Variables
The condition that a variable first appears in the left hand side and the right hand side at the same time (e.g., a=a+1) will not appear in the testcase.
Variable names will only contain char a-z and A-Z and may have different lengths.
After the evaluation of the assembly code, the answers of the variables x, y, z need to be stored in the registers r0, r1, and r2, respectively.

## Slide 9: Example:
Input: x = z + 5
Output: (One of the possible outputs)
MOV r0, [0]
MOV r1, [4]
MOV r2, [8]
MOV r3, 5
ADD r3, r2
MOV r0, r3
EXIT 0
Read initial values from memory
Set a constant value 5 to r3
Add r3 (5) and r2 (z), and store the result to r3
Move the result from r3 to r0 (x)
Program ends

## Slide 10: Error handler
If the expression is illegal, such as
x = + 3 % 5
y = (x+)
Your final output should be
EXIT 1

## Slide 11: Total clock cycles
Each instruction has an expected runtime, which is specified by clock cycles, as shown in the table.
The runtime of a program is the summation of the clock cycles of all instructions.
Example: the following code has 90 clock cycles
MOV r0, 3 10 cc
MOV r1, 5 10 cc
MUL r0, r1 30 cc
MOV r1, 0 10 cc
MOV r2, 0 10 cc
EXIT 0 20 cc

## Slide 12: Contest
The project has 2 parts:
The basic test cases will be provided by TAs
The contest: The code with the less total clock cycles is better. 30 top winners will get extra credits.

## Slide 13: Plagiarism
Definition
  Copying someone else’s work
  Including variable renaming!
Policy
  Perfectly fine to ask questions and discuss
  NOT acceptable to copy part or whole work => zero points on the project
  Automatic tools will be used to catch cheaters
TAs of the two classes will work together to eliminate plagiarisms. Do not cheat!! 

## Slide 14: More details

## Slide 15: Testcase restriction
Only specified variables and signs are allowed.
  + - * / ( ) & | ^ -> valid
  @#$%  invalid, will not appear in the testcase
  x y z 0-9 a-z A-Z -> valid
The result should follow the elementary arithmetic.
  x = 2+3*4, x will be 14
  x = (2+3)*4, x will be 20
A testcase may contain multiple expressions separated by “\n”.

## Slide 16: Program output restrictions
You should print all the assembly code rather than only print the result.
Ex:
  y = 1
  z = 0
  x = y + 5
  One of the possible result will be:
  MOV r0, 0
  MOV r1, 1
  MOV r2, 0
  ADD r0, r1
  MOV r3, 5
  ADD r0, r3
  EXIT 0
  This is a correct result.

## Slide 17: Demo reminder
We will create a contest on NTHUOJ, you can send your code repletely within the time limit.
There will be 20 testcases, each valued 5 points, totally 100.
We will use parser to check the correctness of your output.
If you have any question about the project, feel free to ask your question on iLMS.

## Slide 18: Others
1. Don’t need to strive to optimize some strange expressions, e.g.
x = ((1+1))*((((1+1+1)))) or x = -(-(-1))
2. We only test basic parenthesis, e.g.
x = 2*(3+4)+5
3. Must deal with basic errors using EXIT 1, e.g.
3-1 Extra or missing symbols (ex: x = +-3 or x = y 3)
3-2 Incorrect expression(ex: 1 = 2 + 3 or x + y = 5)
4. If case is valid:
4-1 Satisfy the four fundamental operations of arithmetic
4-2 Can calculate numbers > 10 (e.g. x = 11)
4-3 Can calculate long expressions (e.g. x = 4 -x / z*33+4+ 20*31+10)
5. Test cases with controversy won’t appear (e.g. x = +5 or x = (-(-(-3))) )
Please consider how to use registers and memory correctly.